SURFACE CLEANSER

An Ultra Low Disturbance

Building Solution

Introduction

PRS SURFACE CLEANSER is a  water based concentrate to dilute with water to use as an anti-mould treatment.

It is recommended as a pre-treatment for anti-mould and anti-condensation paint coatings.

DESCRIPTION

PRS SURFACE CLEANSER is a clear concentrated solution designed to be diluted to make a surface treatment for all types of ‘moulds’, on masonry, timber or decorative surfaces.

It is essential to apply this treatment prior to re-painting, as mould can grow through new coatings, even anti-mould formulations.

TECHNICAL DATA

Active Substance

Quaternary Ammonium Halide 10% w/w

Other Components

Water

Corrosion

No action.

Aggressivity to other materials

No known aggressivity

Classification

Irritant.

Special features

·	Convenient 250ml concentrate makes 5 litres

·	Easy to mix

·	Non staining

·	Odourless

·	Non Flammable (conc. & dil.)

·	Non Caustic & Corrosive

·	12 months shelf life

PRS SURFACE CLEANSER

CONCENTRATE

USE

Dilute 1 part to 19 parts of clean water, by volume (250cc of concentrate make 5 litres of gauging solution).

PREPARATION & APPLICATION

Remove all loose surface material and wash down any grease contaminated finishes with a detergent or ‘sugar soap’.

Add the concentrate to the water and apply by brush, sponge or cloth at the rate of 6-8 square metres per litre.

Allow 1-4 hours for drying before applying coatings. For surfaces prone to condensation repeat the treatment as necessary and attempt to reduce the humidity. Badly soiled areas may need a second application.

Property Repair Systems – 01626 331351

DCM/01/08