ANTIMOULD

PAINT ADDITIVE

Special features

·	Add to any paint type

·	Easy to mix

·	Non Flammable

·	Low odour

Introduction

ACS Antimould Paint Additive is a premium quality low odour anti mould concentrate. It prevents mould growth by incorporating the biocide within the paint film itself.

This provides permanent protection, because  the active ingredient does not break down.

DESCRIPTION

ACS Antimould Paint Additive is a colourless concentrate which provides permanent protection to walls and ceilings against mould growth. It can be added to any type of paint.

TECHNICAL DATA

Active Substance

Biocides based on N-Formals and Isothiazolinones Inerts.

Other Components

Glycol

Corrosion

No action (no special priming on metals)

Aggressivity to other materials

None known

Concentration

Allow 1 x 50cc per 2.5 litre of emulsion or gloss paint

WARNING

Do not paper or paint over the anti mould treated paint or you will prevent it from acting and mould will re-grow.

50cc concentrate

USES

As a paint additive to prevent mould growth in paint coatings.

PREPARATION

Thoroughly clean all wall and ceiling surfaces to remove fungal debris and all other loose and organic material (e.g. mouldy wallpaper, etc). Make  good any surface defects.

Wash and clean all surfaces with Antimould Surface Cleaner (250cc makes 5 litres – covers 30–40 square metres) to kill existing mould growth (otherwise this may re-grow and penetrate through the paint film).

Add the concentrate to the paint and thoroughly stir. Paints treated with this product can be applied over wallpaper and can be colour tinted using any proprietary tinting system.

Property Repair Systems

Unit 3, Olympus Business Park, Kingsteignton Road, Newton Abbot, Devon TQ12 2SN  Tel: 01626 331351